Installation Guide

● Access Control for Building

● Telephone line

● Digital Intercom – MT-88

Tador Technologies LTD

Amagshimim 18,

Qiriat Matalon Petach Tikva,

49170

Israel

Phone: +972-3-9226351

Fax: +972-3-9210461

www.tador.com

©2000 Tador Technologies Ltd

All rights reserved

General

The Multiphone MT-88 is a fancy anti vandal encoder for apartments building, condominiums

The main advantage of the system is that you don't need any wires for the unit as it works as a telephone and makes an actual calls

The system is suitable for any area that don't have infrastructure and need an intercom system to communicate

The system can store up to 99 numbers.

Calling charge system (local call without extra cost).

An English friendly LCD display guides the user when

Searching for a particular apartment number or family  Name.

The system provides an excellent sound quality and an

availability for color camera.

Features:

| Basic system controls up to 99 apartments. With 99 individual telephone numbers. | Power failure resistance, keeps the names, settings and access codes in nonvolatile memory |
| --- | --- |
| up to 96 simultaneously different access codes. | Easy installation, programming and operating. |
| environmental and anti vandal resistance. | 16 characters on 2 lines English LCD display. |
| optional bypass exit pushbutton | Illuminated display. |

# Specifications:

| Operating voltage: DC 12V 1000mA * Preferred to use DC Power supply * Preferred power supply with EARTH | Code length: 2-6 keys |
| --- | --- |
| Operating electric or magnetic lock. (normally open or normally close) | Opening time: 1-99 seconds |
| Color: silver or bronze | Size: 288X125X55 (H*W*D) |

Installation:

Make sure the power supply is not connected.

A 100X250 mm opening window should be cut in the mounting surface.

Mount the unit in its place.

Route the following wirings:

- 2 wires from 12 VAC 1000mA power supply.

- 2 wires from optional bypass pushbutton.

- 2 wires from electric lock.

- 2 wires from Telephone line (tip and ring).

Programming:

if not changed, technician code is:123456.

to enter to the programming menu type the following sequence: asterisk, technician code, asterisk.  Press: ( ( 123456 ( (

the programming menu appears. You can navigate among the following screens by pressing the arrows ( (  and leave the menu by pressing the * key or wait for 10 seconds without touching the key pad.

The menu screens:

1. This screen is used to maintain the tenants names

and apartments numbers.

2. This screen is used to maintain the access codes.

3. This screen is used to maintain the master(technical)

Code.

4. This screen is used to maintain the user code.

5. this screen is used to set the: holding, ring,

illumination and door opening timings.

6. This screen is used to change the telephone nymber

by appartment

7. This screen is used to change the remote code used

By Telephone.

8. this screen is used to change the busy tone type

7. This screen is used to change the of ring until the

multi tenant will answer.

- maintaining the tenants names

this screen is used to maintain the tenants names and link them to the apartments numbers.

Scroll the programming menu up or down till this menu appears

press the bell button (

using the arrows buttons scroll among the apartments

numbers, till the apartment number to be defined is

shown.

If names appear on the screen you can run them over.

Name length is limited to 16 characters.

Writing method:

After each character writing the cursor should be proceeded

to move back the cursor use the ‘*’ button.

To proceed use the ‘#’ button.

Each numerical button represents several letters,

as shown in the table. Any cell phone keyboard can assist you to identify the letters.

For instance, to enter the name: “SAM” to apartment number 15

In order to type the letter “S” press “7” four times.

Proceed the next character by pressing the ‘#’  button.

In order to type the letter “A” press “2” once.

Proceed the next character by pressing the ‘#’  button.

In order to type the letter “M” press “6” once.

Proceed the next character by pressing the ‘#’  button.

In order to leave a blank character instead of existing

one: step over the letter to be deleted and press once

the “0” button.

To edit another name – using the arrows scroll to his

apartment number.

To leave the menu press ‘*’  button.

When leaving the menu the system informs it is organizing

the names alphabetically in its memory.

2. Setting or canceling access codes

Up to 96 different access codes could be stored. Valid code length is between 1 to 9 digits.

Recommended length is 4 digits.

Scroll the programming menu up or down till this menu

Appears. press the bell button (

Using the arrows you can navigate among the current codes

and the free spaces.

2.1 Canceling an existing code

in case you want to cancel a code, search it among the

access codes. When found press ‘#’, the code will be deleted

from the system.

2.2 Entering a new code

navigate among the codes screens till you reach a free cell.

Press the new code.

If you need to enter more codes – using the arrows search for a free cell.

To confirm leave this menu by pressing the ‘*’  button.

3. Changing master (technician) Code

recommended  master Code length is 6 digits. Keep the new code with this manual. Access to the programming menu is enabled only with this code.

If the Tech. Code is forgotten, the manufacturer default Tech. Code could be restored By performing the  “Initiation” procedure, detailed in paragraph 6.

The restored code is 123456 it will enable you to enter the

programming menu and change the Tech. Code.

Scroll the programming menu up or down till this menu

Appears. press the bell button (

You can see the current Tech. Code, you can delete it by

pressing the new code or run it over by

press the new code.

To confirm leave this menu by pressing the ‘*’ button.

4. Changing user Code

Recommended user Code length is 6 digits. Keep the new code with this manual. Access to the part of programming Tenant and access codes is enabled only with this code.

This code will enable you to enter the programming menu

and change the users names, users telephones numbers

and change the users access codes.

Scroll the programming menu up or down till this menu

appears press the bell button (

You can see the current Tech. Code , you can delete it by

press the new code or run it over by

press the new code.

To confirm leave this menu by pressing the ‘*’  button.

5. Setting Timings

This screen is used to set the different timing settings.

Scroll the programming menu up or down till this menu

Appears. Press the bell button (

5.1 Setting Delay Time

Delay Time is the time between pressing the access code till the lock opens.

Default time is 0 seconds.

Entering a value will delay the door open command, along

this delay a Beep will be sound.

Run over the current value, by pressing the new value.

To confirm and leave press ‘*’ button. To confirm and move to the next sub menu use the arrows.

5.2 Setting Door Opening Time

Door Opening Time is the time the electric lock will be open. This time should be long enough to reach the door and pull the handle.

During this time a constant Beep will be sound.

(the Beep is needed for silent DC operated locks).

Run over the current value, by pressing the new value.

To confirm and leave this menu press ‘*’ . To confirm and move to the next sub menu use the arrows.

5.3 Setting illumination Time

Illumination Time is the time the display is illuminated after

each key press.

If a constant illumination is needed – enter the value 99.

Run over the current value, by pressing the new value.

To confirm and leave press ‘*’  button. To confirm and move to the next sub menu use the arrows.

5.4 Setting Ring Time

Ring Time /dial is the time the unit send “dialing” sound

(not the tone that sound on the telephone).

Run over the current value, by pressing the new value.

To confirm and leave press ‘*’ button. To confirm and move

to the next sub menu use the arrows.

5.5 Setting talk Time X10 Sec

talk Time is the time the unit keeps the communication until

hang up.(the shown value is multiply by 10 sec)

Run over the current value, by pressing the new value.

To confirm and leave press ‘*’. To confirm and move

to the next sub menu use the arrows.

5.6 Setting View name / Ringing

View name /ring is the time the unit keep dialing name

to display during ring time (value 0 is not recommended).

Run over the current value, by pressing the new value.

To confirm and leave press ‘*’ . To confirm and move

to the next sub menu use the arrows.

5.7 Setting camera time

camera Time is the time the unite hold camera relay upon

ringing.

Run over the current value, by pressing the new value.

To confirm and leave press ‘*’ . To confirm and move

to the next sub menu use the arrows.

6. Changing phones number by apartments

Scroll the programming menu up or down till this menu

Appears. press the bell button (

The shown number is the dialing number 21 to apartment

# 01.

you can delete the number by using ‘#’ key or run it over

by pressing the new telephone number.

Move to next appointment by using ( key or move to previous apartment by using (

key.

Use the ( key to enter 2 sec delay on dialing .(the  “-“ sing is the break sign)

Example : 09-12345 the unit will dial 09 break then 12345.

To confirm leave this menu by pressing the ‘*’  button.

7. Changing remote code using by the telephone

Scroll the programming menu up or down till this menu

Appears. press the bell button (

The shown number is the code use to open the door by

Using the telephone. 
(It is preferred to use two different numbers for door opening)
Max 2 digit to open the door by telephone.

Example to set 56 to open the door via the telephone:

- 123456*

- Choose: 
PROG. Menu
Remote code / TEL
Press : (

- Insert remote code : 56

- Press : *,* ( confirm and exit program mode )

To open the door press key # 5,6 on the telephone during conversation.

8 Changing detection of busy tone

Scroll the programming menu up or down till this menu

Appears. press the bell button (

The shown number is the busy tone detection.

The interval time for 1st detection is 0.5 sec .

the busy tone that repid every 0.5 sec (+/- 20 %) detect

as busy and will stop the converstion.

The unit can detect two saprete busy tone at the same time.

Move to next detection by using ( key or move to previous detection by using (

To confirm leave this menu by pressing the ‘*’  button.

9. Changing number of ring  to answer

Scroll the programming menu up or down till this menu

Appears. press the bell button (

The shown number is the number of ring before the

unit will answer to incoming calls.

you can run it over by pressing the new number/s.

Max 2 digit (Example: 02 ,2, are functionality identical).

To confirm leave this menu by pressing the ‘*’ button.

10. Initiation state

in case the technician Code was forgotten, the manufacturer default code could be restored.

The restored Technician Code is: 123456. using it you can access the programming menu.

Implementation: disconnect the power source.

Using Philips screw driver open the unit’s cover’s screw.

Look for connector JP5 in the circuit board lower left corner.

Place the jumper over the two most left pins (labeled DEFU).

Reconnect the power source carefully. A short conformation Beep will be sound.

Disconnect the power source.

Place the jumper back to the most right pins of connector JP5.

Place the panel back and tighten the screw.

Reconnect the power source.

The procedure is completed, the Technician Code is restored without effect on other data stored in the device.

lay will show who it calls and a double ringing tune will be sound.

11. Checking unit Version :
in case need to know the unit version enter programming menu:
123456* and look for V sign, this state the unit version example :

Version : 1.5 = V1.5

# Text boxes

Illumination

99

Door Opening

05

Delay Time

00

PROG. MENU

TIMINGS (SEC.)

set user code

252525

PROG. MENU

user code

set master code

123456

PROG. MENU

master code

ENTER CODE #04

.

ENTER CODE #04

4568

PROG. MENU

ACCESS CODES

Ring time/dial

03

WAIT . . .

ORGANIZING NAMS!

remote code is:

-5

PROG. MENU

remote code / TEL.

Phone by apr.#01

21

PROG. MENU

Phones #by Apart

Talk time X10 sec

10

Camera time

30

ENTER NAME #15

SAM

| 3 D,E,F | 2 A,B,C | 1 .,-,, |
| --- | --- | --- |
| 6 M,N,O | 5 J,K,L | 4 G,H,I |
| 9 W,X,Y,Z | 8 T,U,V | 7 P,Q,R,S |
| # ( | 0 ( ) | * ( |

ENTER NAME #04

.

PROG. MENU

TENANTS

PROG. MENU

# of ring/answer

PROG. MENU

detect busy tone

View name / Ring

03

PROG. MENU

Remote code /TEL

PROG. MENU

Phones #by Apart.

PROG. MENU

TIMINGS (SEC.)

PROG. MENU

User code

PROG. MENU

master code

PROG. MENU

ACCESS CODES

PROG. MENU

TENANTS

PROG. MENU

Detect busy tone

Busy 1 x0.1 sec

5

Busy 2 x0.1 sec

6

PROG. MENU

# of ring /answer

number of rings :

02

PROG, MENU  V1.5

Tenants